## Slide 1: Graham Price PhD Dissertation Defense
Advised by Dr. Manish Vachharajani
Department of Electrical, Computer, and Energy Engineering
University of Colorado at Boulder
04/08/2011
Dynamic Trace Analysis with ZDDs
Notes: Intro..

## Slide 2: Solving Puzzles with Dynamic Analysis
(Intel Quad Core)
(Intel Single Core)
Hot Code Detection
Instruction Level Parallelism
Loop Level Dependencies
Thread Level Speculation
Analysis
Code
Test
Notes: ----- Meeting Notes (4/7/11 21:10) -----
Traditional dynamic analysis works well when you know exactly what you are looking, but makes exploration of opportunities difficult.

## Slide 3: Hypothesis
ZDD-based dynamic trace analysis can identify hot-code paths, irrelevant instructions, and potential coarse-grained thread level parallelism in sequential codes, and thus find opportunities for program optimization.
Notes: ----- Meeting Notes (4/7/11 21:10) -----
This work focuses on a ZDD-based dynamic trace analysis framework that permits exploration.

## Slide 4: Dynamic Analysis Puzzle Solving
Find Opportunities
Scalable Framework
Single Core Analysis
Multi Core Analysis
Notes: ----- Meeting Notes (4/7/11 21:10) -----
The are four main components to building this framework - techniques to find opportunities, techniques for multicore analysis, techniques for single core analysis, and finally data structures and algorithms to make all of these scalable.

## Slide 5: Dynamic Analysis Puzzle Solving
Find Opportunities
Scalable Framework
Single Core Analysis
Multi Core Analysis

## Slide 6: DIN vs. Ready Time
li r1, &fibarr
mov r2, 8
mov r4, 1
mov r3, 1
add r5,r3,r4
st 0(r1),r5
mov r3,r4
mov r4,r5
addi r2,r2,-1
addi r1,r1,4
bnz r2, loop
add r5,r3,r4
st 0(r1),r5
mov r3,r4
…
0xbee0
0xbee4
Instruction
Mem Addr
0
1
2
3
4
5
6
7
8
9
10
11
12
13
DIN
0
1
2
3
4
5
6
7
8
9
10
11
12
13
DIN
Ready Time
0
1
2
3
4
5
6
7
8
9
10
11
12
13
0
1
2
3
12
4
6
8
9
5
7
10
13
11

## Slide 7: Distant ILP Characteristics
Divergent lines indicate parallel “threads” of execution
Independent chains of dependences (DDCs)
DINxRDY plot for 254.gap
Multiple
Dep. chains
Postiff et al. (JILP 1999)
Iyer et al. (EPIC 2005)
Notes: The DDCs overlap in time, and can be potential threads

## Slide 8: Compression Methods
Run Time Linear Compression
  Requires trace compression/decompression
  TCGen (Burtscher and Sam, CGO 2005)
Hierarchical Grammars
  Requires full grammar traversal for some analysis
  SEQUITUR (Nevill-Manning and Witten, DCC 1997)
Stride Compression
  Locates dynamic dependence conflicts in loops
  SD3 (Kim et. al., Micro 2010)

## Slide 9: Binary Decision Diagram (BDD)
False Arc
Inverting
False Arc
True Arc
F(X,Y,Z,W) = X*Y*Z*W
0
Y
W
Z
W
Z
Z
Z
0
0
0
0
0
0
0
0
Y
W
Z
W
Z
Z
Z
0
0
0
0
1
0
0
X
1
X
Y
W
Z

## Slide 10: Trace BDD Construction
(0,0)
0
1
2
3
4
5
6
7
8
9
10
11
12
13
DIN
Ready Time
0
1
2
3
4
5
6
7
8
9
10
11
12
13
(0,1)
(0,2)

## Slide 11: Trace BDD Construction
(X’ * Y’ * Z’ * W)
(X’ * Y’ * Z’ * W’)
ftrace = (X’ * Y’ * Z’ * W’) + (X’ * Y’ * Z’ * W) + (X’ * Y’ * Z * W’)
(0,0)
(00,00)
(0,1)
(00,01)
(X’ * Y’ * Z * W’)
(0,2)
(00,10)
Data Tuple
Binary Tuple
Boolean Function

## Slide 12: BDD Trace Representation
Compression ranges from 16x to over 60x
BDD Based Analysis
  [Whaley and Lam, PLDI 2004]

## Slide 13: Quad Tree Image Rendering

## Slide 14: BDDs as Quad-Trees

## Slide 15



175.vpr Case Study

## Slide 16: DINxRDY Visualization

## Slide 17: Dynamic Slicing

## Slide 18: DINxRDY to Source

## Slide 19: ParaMeter - Extracting TLP












Time
Time

## Slide 20: Dynamic Analysis Puzzle Solving
Find Opportunities
Scalable Framework
Single Core Analysis
Multi Core Analysis

## Slide 21: BDD Creation Time
Chart: 
| 164.gzip | 175.vpr | 176.gcc | 181.mcf | 186.crafty | 197.parser | 252.eon | 253.perlbmk | 254.gap | 255.vortex | 256.bzip2 | 300.twolf
BDD Creation (hours) | 16.9572 | 24.1964 | 32.2603 | 15.8439 | 0.41528 | 22.1692 | 20.3614 | 18.0536 | 16.5436 | 0.0069444 | 0.13028 | 21.4183
250 million instructions
(hrs)

## Slide 22: Trace BDD Construction
fd1 = (X’ * Y’ * Z’ * W)
fd0 = (X’ * Y’ * Z’ * W’)
=
+
ftrace = (X * Y * Z * W) + (X’ * Y’ * Z’ * W’)
1
X
Y
Z
1
X
Y
W
Z
1
X
Y
W
Z

## Slide 23: BDD Garbage Collection Time
Chart: 
| 164.gzip | 175.vpr | 176.gcc | 181.mcf | 186.crafty | 197.parser | 252.eon | 253.perlbmk | 254.gap | 255.vortex | 256.bzip2 | 300.twolf
Garbage Collection | 34744 | 60352 | 86119 | 33083 | 505 | 51172 | 46865 | 41291 | 34420 | 10 | 97 | 51914
Other Creation | 26302 | 26755 | 30018 | 23955 | 990 | 28637 | 26436 | 23702 | 25137 | 15 | 372 | 25192

## Slide 24: Zero-Suppressed BDD (ZDD)
BDDs
Remove isomorpic graphs
Skip and remove nodes whose pointers point to the same child
ZDDs
Remove isomorpic graphs
Remove nodes whose “then” arc points to the constant 0

## Slide 25: Trace ZDD Gains
~ 20% Reduction
Chart: 
| 164.gzip | 175.vpr | 176.gcc | 181.mcf | 186.crafty | 197.parser | 252.eon | 253.perlbmk | 254.gap | 255.vortex | 256.bzip2 | 300.twolf
ZDD Node Count | 14776031 | 26758473 | 47191021 | 13371337 | 1426447 | 20298664 | 13438978 | 15447265 | 18167754 | 193184 | 101730 | 26470707
BDD Node Count | 20191795 | 39488720 | 65452369 | 18857151 | 1989019 | 28928181 | 19243812 | 22507110 | 24067457 | 260701 | 138353 | 36674682

## Slide 26: Trace ZDD Construction
Over 9x faster than BDD construction!
Chart: 
| 164.gzip | 175.vpr | 176.gcc | 181.mcf | 186.crafty | 197.parser | 252.eon | 253.perlbmk | 254.gap | 255.vortex | 256.bzip2 | 300.twolf
ZDD Time (min) | 191.45 | 261.65 | 410.2 | 166.5833 | 3.65 | 223.2 | 196.95 | 196.2167 | 169.0833 | 0.083333 | 0.83333 | 235.4167
BDD Time (min) | 1017.4333 | 1451.7833 | 1935.6167 | 950.6333 | 24.9167 | 1330.15 | 1221.6833 | 1083.2167 | 992.6167 | 0.41667 | 7.8167 | 1285.1

## Slide 27: Scalable Framework







## Slide 28: Scalable Framework

## Slide 29: Scalable Framework
175.vpr
164.gzip
176.gcc
197.parser
252.eon
255.vortex

## Slide 30: Dynamic Analysis Puzzle Solving
Find Opportunities
Scalable Framework
Single Core Analysis
Multi Core Analysis

## Slide 31: Hot Code Analysis




## Slide 32: Irrelevant Instruction Detection
Reaches the end
Produces an output

## Slide 33: Irrelevant Instruction Detection
SPEC INT 2006
Compare –O0 and –O2

## Slide 34: Dynamic Analysis Puzzle Solving
Find Opportunities
Scalable Framework
Single Core Analysis
Multi Core Analysis

## Slide 35: 445.gobmk TLP Region Selection

## Slide 36: 445.gobmk Naïve Parallelism
Overlap on RDY
DINs

## Slide 37: 445.gobmk Naïve Parallel Count
Nine Threads

## Slide 38: Inter-Region Dependencies
Reverse Slice
Forward Slice
Intersection
Intersection - Days to Weeks

## Slide 39: Inter-Region Dependency Chopping
Reverse Slice
Forward
Edge Slice
Chop
Chop – Hours to Days

## Slide 40: 445.gobmk Inter-Region Dependencies

## Slide 41: Coarse-Grained Parallelism
Parallel Instructions
Thread Count

## Slide 42: Fine-Grained Thread Level Speculation
allLines := read()
foreach line in allLines
processDataA(line)
foreach line in allLines
processDataB(line)
Max n Cores

## Slide 43: Coarse-Grained Thread Level Parallelism
allLines := read()
foreach line in allLines
processDataA(line)
foreach line in allLines
processDataB(line)
Max 2 Cores

## Slide 44: Fine-and-Coarse Grained Harmony
allLines := read()
foreach line in allLines
processDataA(line)
foreach line in allLines
processDataB(line)
Max 2n Cores

## Slide 45: Dynamic Analysis Puzzle Solving
Find Opportunities
Scalable Framework
Single Core Analysis
Multi Core Analysis

## Slide 46: What Just Happened?
Traces to BDDs
Visualized BDDs
Scalability - ZDDs
Hot Code
Irrelevant Code
Coarse-Grained TLP Survey
=
+
175.vpr
164.gzip
176.gcc
197.parser
252.eon
255.vortex

## Slide 47: Contributions
A ZDD-based trace compression algorithm with tuning for large traces, resulting in a 25% reduction in BDD size and a 9x reduction in trace compression time.
A ZDD-based iterative analysis for locating irrelevant instruction dependencies
A method to quickly explore coarse-grained parallelism in serial applications.
A ZDD-based dependence graph chopping algorithm need for the aforementioned method.
A survey of coarse-grained thread level parallelism in the SPEC INT 2006 benchmarks that shows up to 44% of instructions may be extractable as coarse grain TLP.

## Slide 48: Questions?
Price and Vachhajarani. A Case for Compressing Traces with BDDs. CAL 2006
Price, Giacomoni, Vachharajani. Visualizing Potential Parallelism in Sequential Programs. PACT 2008
Price and Vachharajani. Large Program Trace Analysis and Compression with ZDDs. CGO 2010
Price and Vachharajani. A Survey of Coarse-Grained Thread Level Parallelism in SPEC 2006. PACT 2011 [Submitted]

## Slide 49: Bonus Slides

## Slide 50: TLP Survey – 401.bzip2
13% Naïve Improvement
12% Improvement w/o DDG Interference

## Slide 51: Coarse-Grained TLP and TLS
Best TLS performance for SPEC 2006 (Kejariwal PPOPP 2007)

## Slide 52: Dynamic DDG Chopping
global integer A,B
1: string S = read(“myint.txt”)
2: integer C = integer(S)
3: A = someFunc()
4: B = A + C
Dynamic Dependence Graph (DDG)
1
4
2
3

## Slide 53: Reverse Slicing
global integer A,B
Simulated Thread γ
1: string S = read(“myint.txt”)
2: integer C = integer(S)
4: B = A + C
Simulated Thread β
3: A = someFunc()

## Slide 54: Dynamic DDG Chopping
global integer A,B
Region γ
1: string S = read(“myint.txt”)
2: integer C = integer(S)
4: B = A + C
Region β
3: A = someFunc()
Forward Slice
Reverse Slice

## Slide 55: Performance Gain Conflicts



## Slide 56: Irrelevant Instruction Elimination
DINs
Output
NULL
DINs
Output
NULL
DINs
Output
NULL
DINs
Output
NULL

## Slide 57: Case Study - Select and Slice 







## Slide 58: Case Study - Reverse Slice
Perform a single reverse data dependence slice on the selected region




## Slide 59: Binary Decision Diagram (BDD)
False Arc
Inverting
False Arc
True Arc
F(X,Y,Z,W) = X*Y*Z*W
0
Y
W
Z
W
Z
Z
Z
0
0
0
0
0
0
0
0
Y
W
Z
W
Z
Z
Z
0
0
0
0
1
0
0
X
0

## Slide 60: The BDD Data Structure
False Arc
Inverting
False Arc
True Arc
F(X,Y,Z,W) = X*Y*Z*W
Y
W
Z
W
Z
Z
Z
Y
W
Z
W
Z
Z
Z
1
X
Z
0

## Slide 61: The BDD Data Structure
False Arc
Inverting
False Arc
True Arc
F(X,Y,Z,W) = X*Y*Z*W
Y
W
W
Y
W
W
Z
1
X
Z
0
W

## Slide 62: The BDD Data Structure
False Arc
Inverting
False Arc
True Arc
F(X,Y,Z,W) = X*Y*Z*W
Y
Y
W
Z
1
X
Z
0
W
0

## Slide 63: The BDD Data Structure
False Arc
Inverting
False Arc
True Arc
F(X,Y,Z,W) = X*Y*Z*W
Y
W
Z
1
X
0
1
X
Y
W
Z

## Slide 64: Trace BDD Construction Cont..
Unique Table
fd1 = (X’ * Y’ * Z’ * W)
1
X
Y
W
Z
fd0 = (X’ * Y’ * Z’ * W’)
=
+
ftrace = (X’ * Y’ * Z’ * W’) + (X’ * Y’ * Z’ * W)
1
X
Y
W
Z
ftrace = (X’ * Y’ * Z’ * W’)
1
1
Itrace = 0
1
X
Y
W
Z
1
X
Y
Z
Compute Cache
Dead Nodes

## Slide 65: Trace BDD Construction Cont..
1
X
Y
W
Z
=
+
ftrace
1
X
Y
Z
1
X
Y
W
Z
fd3 = (X’ * Y’ * Z * W’)
Unique Table
Compute Cache
Dead Nodes

## Slide 66: BDD Garbage Collection Time

## Slide 67: ZDDs
BDDs
Remove isomorpic graphs
Skip and remove nodes whose pointers point to the same child
ZDDs
Remove isomorpic graphs
Remove nodes whose “then” arc points to the constant 0

## Slide 68: Trace ZDD Construction
fd1 = (X’ * Y’ * Z’ * W)
fd0 = (X’ * Y’ * Z’ * W’)
=
+
ftrace = (X’ * Y’ * Z’ * W’) + (X’ * Y’ * Z’ * W)
1
0
1
W
0
1
W
0
Compute Cache
Dead Nodes
Unique Cache

## Slide 69: Trace ZDD Construction
fd3 = (X’ * Y’ * Z * W’)
=
+
ftrace
1
Z
0
1
W
0
ftrace (new)
1
W
0
Z
Unique Cache
Compute Cache
Dead Nodes

## Slide 70: Trace ZDD Gains
~ 20% Reduction

## Slide 71: Trace ZDD Losses
3x Slower!

## Slide 72: Trace ZDD Construction
fd3 = (X’ * Y’ * Z * W’)
=
+
ftrace
1
Z
0
1
W
0
ftrace (new)
1
W
0
Z
Unique Cache
Compute Cache
Death Row

## Slide 73: Trace ZDD Construction
DIN x RDY Tuples
Over 9 times faster!